## Slide 1
Working and Connections of 3-Axis MEMS Gyroscope & Mixed Step-Down Transformer
Precision Sensing and Power Regulation in Modern Systems
Presenter Name: [Your Name]
Transformer

## Slide 2
Overview of Components
The sensor and power unit
The Sensor: 3-Axis MEMS Digital Gyroscope
Detects angular velocity on X, Y, and Z axes.
Essential for drones, stabilization, and gaming.
Measures rotational motion precisely in real time.
The Power/Actuator Component: Mixed Step-Down Transformer
Converts high-voltage AC into multiple lower-voltage AC outputs.
Provides the energy source for the control system.
Supports different voltage levels for connected devices.
MEMS IC
Multi-tap Transformer

## Slide 3
Working of 3-Axis MEMS Gyroscope
Core principle is the Coriolis Effect
Principle
The Coriolis Effect is the core operating principle.
Tiny silicon structures vibrate at a high frequency inside the chip.
When the device rotates, Coriolis force causes a displacement of these structures.
This movement changes electrical capacitance between the moving and fixed parts.
Output
The capacitance variation is converted by an onboard ASIC.
Digital data is generated as angular velocity values in degrees/sec.
These values are used to detect rotation on the X, Y, and Z axes.
The result is precise orientation and stabilization feedback.
Proof Mass
Coriolis Force

## Slide 4
Connections of the MEMS Gyroscope
Most digital gyroscopes use I2C
Pin Functions
VCC: Power input (3.3V or 5V DC).
GND: Ground reference.
SCL: Serial clock signal for synchronization.
SDA: Serial data line for sensor output.
AD0: Address select pin for multiple sensors.
MCU
Gyro
SCL SDA VCC GND AD0

## Slide 5
Working of Mixed Step-Down Transformer
Based on mutual induction and Faraday’s Law
Operating Principle
Mutual induction is the fundamental concept.
AC current in the primary coil creates a magnetic field in the core.
This induces a voltage in the secondary coil.
A step-down effect occurs because the secondary has fewer turns.
A mixed transformer has multiple taps to provide different output voltages.
6V 12V 24V taps

## Slide 6
Connections of a Mixed Transformer
Primary and secondary wiring
Primary Side
Connected to the AC mains (110V/220V).
This side receives the high-voltage input supply.
Proper isolation and insulation are essential for safety.
Secondary Side (Mixed Taps)
0V: common reference / shared ground.
Tap 1: e.g., 6V for logic boards and sensors.
Tap 2: e.g., 12V for relays or small motors.
Fuse: Always use a safety fuse on the primary side.
Primary AC input → Transformer → 0V / 6V / 12V / 24V taps

## Slide 7
Connecting Sensor to Transformer (The Bridge)
AC to DC conversion and regulation
Problem
The transformer produces AC, but the gyroscope requires DC power.
A direct connection would not work for the sensor electronics.
Connection Path
Transformer Tap: 6V AC output.
Bridge Rectifier: Converts AC into pulsating DC.
Filter Capacitor: Smooths the pulsating supply.
Voltage Regulator: Provides a steady 5V DC to the gyroscope.
Transformer → Rectifier → Filter Capacitor → Voltage Regulator → MEMS Gyroscope

## Slide 8
Practical Application Example
Camera gimbal stabilizer system
System Role of Transformer
Powers motors and the control board.
Provides stable source voltages for multiple functions.
System Role of Gyroscope
Detects camera tilting and angular motion.
Sends orientation feedback to the controller.
The controller drives motors to resist unwanted motion.

## Slide 9
Precautions and Troubleshooting
Reliable operation and safety
MEMS Gyroscope Precautions
Sensitive to mechanical vibrations; mount on a damping pad.
Keep sensor cabling short and shielded if possible.
Avoid noisy power lines near the signal pins.
Transformer Precautions
Use proper insulation and heat dissipation.
Keep it away from digital sensor wires to reduce EMI.
Ensure airflow and avoid overheating.
Install a fuse on the primary side for safety.

## Slide 10
Conclusion
Final summary
System Roles
The 3-Axis MEMS Gyroscope is the “eyes” of the system, sensing orientation.
The Mixed Step-Down Transformer is the “heart,” providing varied power levels.
Key Insight
Integrating them correctly requires clean AC-to-DC conversion and regulated voltages.
This ensures both sensing accuracy and stable power delivery.
The combined design enables reliable control in modern systems.
Questions?